## Slide 1
Tar Heel Safety: Liquid Nitrogen
Asphyxiation
  Displaces oxygen in confined spaces
  Ensure good ventilation during use and transport
Cold burns/frostbite
  Use cryogenic gloves, in addition to traditional PPE to prevent cold burns
  Fill containers slowly to prevent splashing
Condensing Liquid N2, O2, or Ar is possible
  N2 boiling point: -196 ⁰C
  O2 boiling point: -183 ⁰C
  Ar boiling point: -186 ⁰C
  Condensed gases can create a potentially flammable or explosive condition and is possible when using glovebox traps, Schlenk lines, etc.
  If present, alert lab members/safety officers/PI, replace traps, turn vacuum back on, set up blast shield, evacuate lab
Prevent Pressure Build-up
  Only store in approved vessels, like dewars. Never store in closed vessels.
Discussion Questions: How does your lab use liquid nitrogen? What safety concerns should you consider when using liquid nitrogen?
Resources: https://www.monash.edu/ohs/info-docs/chemical-management/handling-and-storage-of-liquid-nitrogen